## Slide 1: CS61C: Great Ideas in Computer Architecture (aka Machine Structures)
Lecture 25: Data-level Parallelism
Instructors: Dan Garcia, Justin Yokota

## Slide 2: Agenda
Why Parallelism?
Data Level Parallelism: SIMD
Applying SIMD to Matrix Multiplication

## Slide 3: Computing in the News
Cleaning Up the Atmosphere with Quantum Computing
The amount of carbon dioxide in the atmosphere increases daily with no sign of stopping or slowing. Too much of civilization depends on the burning of fossil fuels, and even if we can develop a replacement energy source, much of the damage has already been done. Without removal, the carbon dioxide already in the atmosphere will continue to wreak havoc for centuries.
Atmospheric carbon capture is a potential remedy to this problem. It would pull carbon dioxide out of the air and store it permanently to reverse the effects of climate change. Practical carbon capture technologies are still in the early stages of development, with the most promising involving a class of compounds called amines that can chemically bind with carbon dioxide. Efficiency is paramount in these designs, and identifying even slightly better compounds could lead to the capture of billions of tons of additional carbon dioxide.
In AVS Quantum Science, by AIP Publishing, researchers from the National Energy Technology Laboratory and the University of Kentucky deployed an algorithm to study amine reactions through quantum computing. The algorithm can be run on an existing quantum computer to find useful amine compounds for carbon capture more quickly.
“We are not satisfied with the current amine molecules that we use for this [carbon capture] process,” said author Qing Shao. “We can try to find a new molecule to do it, but if we want to test it using classical computing resources, it will be a very expensive calculation. Our hope is to have a fast algorithm that can screen thousands of new molecules and structures.”
Any computer algorithm that simulates a chemical reaction needs to account for the interactions between every pair of atoms involved. Even a simple three-atom molecule like carbon dioxide bonding with the simplest amine, ammonia, which has four atoms, results in hundreds of atomic interactions. This problem vexes traditional computers but is exactly the sort of question at which quantum computers excel.
Notes: Source: https://publishing.aip.org/publications/latest-content/cleaning-up-the-atmosphere-with-quantum-computing/

## Slide 4: Why Parallelism?
To answer this question, it's useful to take a look at modern supercomputers
Often large warehouse-scale systems, which when used properly can handle extremely fast/large computations
  Berkeley's Savio Cluster
  Google/Amazon computing warehouses
Personal computers will generally have similar structures at a smaller scale
My computer:
  2 GHz clock cycle
  16 GB RAM
  64-bit Intel CPU using x64 (the 64-bit version of x86 assembly)

## Slide 8: Higher Clock Speed?
The speed of light is ~300,000,000 m/s
  1 GHz = 1/1,000,000,000 s, so 1 clock cycles per nanosecond
  3e8 m/s * 1s/1e9 ns = 0.3 m/ns
Light travels 30 cm = about one foot in one nanosecond
My clock cycle is 2 GHz, which is a clock cycle every half-nanosecond
Conclusion: My computer's running so fast that the concept of simultaneity would break down if my CPU was larger than my hand
A warehouse is larger than my hand (I hope), so it would be physically impossible for a supercomputer to run at a significantly faster clock speed

## Slide 9: Faster Memory Accesses/More Transistors?
Not significantly different
Magnetic-disk based memory accesses also are near physical limits
More transistors = more heat = silicon starts to melt
Small improvements possible, but not ~1000x better.

## Slide 10: More complicated operations?
Depends on the architecture
  For RISC-V, it's counterproductive to have more complicated operations
  For CISC architectures, this is actually feasible
This leads to SIMD operations (today's topic)
Still can only get ~4-8x better results than my PC, so relatively low effect.

## Slide 11: More computers?
This is the biggest difference.
My computer has 12 independent CPUs that can run separate programs
The Savio cluster has 3600 CPUs, with each CPU just as powerful as one of my CPUs
Therefore, in order to gain any benefits from using a supercomputer, we need to know how to get many computers to work together on the same problem

## Slide 12: Why Parallelism?
Overall, our goal is to continue increasing the amount of computation that can be done per unit time.
Recall the "Iron Law" of Processor Performance, which dictates the speed a program runs on one processor. In order to speed up our code, we need to improve one of:
Instructions/Program
  Either we reduce the work we do to solve the problem, or
  We increase the amount of work we do per instruction
Cycles/Instruction
Time/Cycle
Time | = | Instructions | Cycles | Time
Program |  | Program | Instruction | Cycle

## Slide 13: Toy Example: Vector Sum
We have two 4-D vectors whose components are 8-bit numbers
Goal: Determine the sum of the two vectors
For the following example, inputs stored at 0(a0) and 0(a1), and output saved to 0(a2)
0b0000 0001 | 0b0000 0010 | 0b0000 0011 | 0b0000 0100
0b0000 0101 | 0b0000 0110 | 0b0000 0111 | 0b0000 1000
0b0000 0110 | 0b0000 1000 | 0b0000 1010 | 0b0000 1100

## Slide 14: Toy Example: Vector Sum: Naive
lb t0 0(a0) lb t0 1(a0) lb t0 2(a0) lb t0 3(a0) lb t1 0(a1) lb t1 1(a1) lb t1 2(a1) lb t1 3(a1) add t0 t0 t1 add t0 t0 t1 add t0 t0 t1 add t0 t0 t1 sb t0 0(a2) sb t0 1(a2) sb t0 2(a2) sb t0 3(a2)
16 total instructions. Can we do better?
0b0000 0001 | 0b0000 0010 | 0b0000 0011 | 0b0000 0100
0b0000 0101 | 0b0000 0110 | 0b0000 0111 | 0b0000 1000
0b0000 0110 | 0b0000 1000 | 0b0000 1010 | 0b0000 1100

## Slide 15: Toy Example: Vector Sum: Single Add
Solution: If we treat these arrays as 32-bit integers, we can add with one operation, and do this in 4 instructions.
lw t0 0(a0) lw t1 0(a1) add t0 t0 t1 sw t0 0(a2)
0b0000 0001 | 0b0000 0010 | 0b0000 0011 | 0b0000 0100
0b0000 0101 | 0b0000 0110 | 0b0000 0111 | 0b0000 1000
0b0000 0110 | 0b0000 1000 | 0b0000 1010 | 0b0000 1100

## Slide 16: Toy Example: Vector Sum: Vectorized Add
This doesn't quite work, because overflow on one element affects other elements. So we need to create a slightly different instruction that ignores overflow every 8th bit.
New instruction should take about as long as a single add instruction, since the circuit's similar
lw t0 0(a0) lw t1 0(a1) vec_add t0 t0 t1 sw t0 0(a2)
0b0000 0001 | 0b0000 0010 | 0b0000 0011 | 0b0000 0100
0b0000 0101 | 0b0000 0110 | 0b0000 0111 | 0b0000 1000
0b0000 0110 | 0b0000 1000 | 0b0000 1010 | 0b0000 1100

## Slide 17: SIMD Instructions
Instead of doing math on one number at a time, we can instead do math on several numbers at a time, in a single clock cycle
Known as SIMD instructions (Single-Instruction, Multiple Data) or vector instructions
Use specialized "vector" registers which store 128, 256, or even 512 bits
SIMD instructions act as extensions to the base instruction set, with different systems supporting different SIMD instructions.
Generally speaking, most of the speedup comes not from doing four math operations at a time, but instead from doing a large memory load/store at a time.

## Slide 18: SIMD Instructions
Caveats: Each instruction needs its own circuitry, so we're limited to the set of instructions that came with the CPU
  RISC-V doesn't have a standard vector library, so we're using x86's vector operators here.
  In practice, this doesn't matter too much since arithmetic syntax works similarly to RISC-V
There's still only one PC, so we can't vectorize branch or jump instructions
  Lab discusses a way to get around that using the equivalent of slt
Since we only have limited instructions available, we can't do different math operations to vector components, and we can only easily load consecutive blocks of memory to a vector
  Note that most programs spend the majority of their time loading/storing instead of doing math, because loads and stores can take hundreds of cycles to resolve
Large vectors require significant amounts of circuitry, so they are expensive to implement, and often have higher cycles/instruction than standard instructions

## Slide 19: Intel Intrinsics
SSE library
  64- and 128-bit registers: 4 32-bit integers at a time or 2 doubles at a time
AVX library
  256-bit registers: 8 32-bit integers at a time or 4 doubles at a time
AVX-2 library
  Extension of the AVX library, with more supported instructions
AVX-512 library
  512 bit registers
  Big enough that it tends to cause throttling issues, so Intel's been quietly trying to kill this library
  Not covered in this class, and not available on hive machines.

## Slide 20: Intel Intrinsics: Types
__m256
  256 bit register for storing floats
__m256d
  256 bit register for storing doubles
__m256i
  256 bit register for storing 32-bit integers
__m128, __m128d, __m128i
  128 bit registers
Each type corresponds directly to a type of SIMD register (note that x86 has different sets of registers for floats, doubles, and integers).
Used similarly to variables, but directly are associated with available registers, so you can't just initialize a bunch of them (or an array of them)

## Slide 21: Intel Intrinsics: Instructions
Generally of the format:
_<register size>_<instruction>_<component_type>
Ex. _mm256_add_epi32 adds two 256-bit vectors, treating the vectors as arrays of 32-bit integers.
Ex. _mm_load_ps loads 4 consecutive floats into a 128-bit register from the given memory address. The memory address must be aligned to a 16-byte boundary (loadu allows for nonaligned addresses, but is slower)
More instructions: https://www.intel.com/content/www/us/en/docs/intrinsics-guide/index.html
Looks like C functions, but programming with them feels more like assembly

## Slide 22: Vector Sum (128-bit registers, 32-bit integers
__mm128i avec = _mm_load_si128(a); __mm128i bvec = _mm_load_si128(b); __mm128i sum = _mm_add_epi32(avec, bvec); _mm_store_si128(c, sum);
0x0000 0001 | 0x0000 0002 | 0x0000 0003 | 0x0000 0004
0x0000 0005 | 0x0000 0006 | 0x0000 0007 | 0x0000 0008
0x0000 0006 | 0x0000 0008 | 0x0000 000A | 0x0000 000C

## Slide 23: Common mistakes when working with SIMD instructions
Trying to directly access a 32-bit chunk of a SIMD vector (such as through typecasting)
  Need to do an explicit load/store, since registers are different from memory
Trying to _mm_load or _mm_store with unaligned addresses
  Use loadu or storeu if you must, or try to get your addresses aligned
  For mallocs, aligned_alloc gives you an aligned address
  For local variables, you can set an attribute (example shown in slides)
Forgetting the tail case
  If your data isn't an array whose length is a multiple of your vector size, you need to handle the last iterations of your dataset one-by-one instead of 4 at a time.
Using too many vectors (or creating a large array of vectors)
  Ends up throttling your code because the compiler ends up trying to load/store SIMD vectors to the stack a bunch of times.

## Slide 24: Applying DLP to Matrix Multiply
Each element of the product array is the result of dot product-ing two arrays.
Would be useful to compute one element at a time; however, we can only load data that's consecutive in memory
Therefore, we need to start by transposing the second matrix
 |  |  |  |  | 17 | 18 | 19 | 20
 |  |  |  |  | 21 | 22 | 23 | 24
 |  |  |  |  | 25 | 26 | 27 | 28
 |  |  |  |  | 29 | 30 | 31 | 32
1 | 2 | 3 | 4 |  |  |  |  | 
5 | 6 | 7 | 8 |  |  |  |  | 
9 | 10 | 11 | 12 |  |  |  |  | 
13 | 14 | 15 | 16 |  |  |  |  | 

## Slide 25: Applying DLP to Matrix Multiply
How do we compute the dot product quickly?
 |  |  |  |  | 17 | 21 | 25 | 29
 |  |  |  |  | 18 | 22 | 26 | 30
 |  |  |  |  | 19 | 23 | 27 | 31
 |  |  |  |  | 20 | 24 | 28 | 32
1 | 2 | 3 | 4 |  |  |  |  | 
5 | 6 | 7 | 8 |  |  |  |  | 
9 | 10 | 11 | 12 |  |  |  |  | 
13 | 14 | 15 | 16 |  |  |  |  | 

## Slide 26: Applying DLP to Matrix Multiply
Let's say we want to find the dot product of the two rows. How do we do this efficiently? (Assume the arrays are aligned)
Step 1: Load 0s into v3:
__m128 v3 = _mm128_set1_ps(0);
1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19
1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
v1 |  |  |  |  | v2 |  |  |  |  | v3 |  |  |  |  | mem |  |  | 

## Slide 27: Applying DLP to Matrix Multiply
Step 2: Load the first four numbers of each input into v1 and v2, respectively
__m128 v1 = _mm128_load_ps(&arr); __m128 v2 = _mm128_load_ps(&arrtwo);
1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19
1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
v1 |  |  |  |  | v2 |  |  |  |  | v3 |  |  |  |  | mem |  |  | 
 |  |  |  |  |  |  |  |  |  | 0 | 0 | 0 | 0 |  |  |  |  | 

## Slide 28: Applying DLP to Matrix Multiply
Step 3: Multiply v1 and v2 together, and add that to v3
  This procedure is so common, there's a single instruction to do this! (Well, for floats and doubles only)
v3 = _mm256_fmadd_ps(v1, v2, v3);
1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19
1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
v1 |  |  |  |  | v2 |  |  |  |  | v3 |  |  |  |  | mem |  |  | 
1 | 2 | 3 | 4 |  | 1 | 1 | 1 | 1 |  | 0 | 0 | 0 | 0 |  |  |  |  | 

## Slide 29: Applying DLP to Matrix Multiply
Step 4: Repeat for the majority of the array
int i; for(i = 0; i < arrlen/4*4;i+=4) { __m128 v1 = _mm128_load_ps(arr+i); __m128 v2 = _mm128_load_ps(arrtwo+i); v3 = _mm256_fmadd_ps(v1, v2, v3); }
1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19
1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
v1 |  |  |  |  | v2 |  |  |  |  | v3 |  |  |  |  | mem |  |  | 
1 | 2 | 3 | 4 |  | 1 | 1 | 1 | 1 |  | 1 | 2 | 3 | 4 |  |  |  |  | 

## Slide 30: Applying DLP to Matrix Multiply
Step 5: Store the results in memory somewhere.
//Force alignment float mem[4] __attribute__ ((aligned (32))); _mm128_store(mem, v3);
1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19
1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
v1 |  |  |  |  | v2 |  |  |  |  | v3 |  |  |  |  | mem |  |  | 
1 | 2 | 3 | 4 |  | 1 | 1 | 1 | 1 |  | 28 | 32 | 36 | 40 |  |  |  |  | 

## Slide 31: Applying DLP to Matrix Multiply
Step 6: Resolve the tail case
for(;i<arrlen;i++) { mem[0]+=arr[i]*arrtwo[i]; }
1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19
1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
v1 |  |  |  |  | v2 |  |  |  |  | v3 |  |  |  |  | mem |  |  | 
1 | 2 | 3 | 4 |  | 1 | 1 | 1 | 1 |  | 28 | 32 | 36 | 40 |  | 28 | 32 | 36 | 40

## Slide 32: Applying DLP to Matrix Multiply
Step 7: Return the sum of mem
return mem[0]+mem[1]+mem[2]+mem[3];
1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19
1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
v1 |  |  |  |  | v2 |  |  |  |  | v3 |  |  |  |  | mem |  |  | 
1 | 2 | 3 | 4 |  | 1 | 1 | 1 | 1 |  | 28 | 32 | 36 | 40 |  | 82 | 32 | 36 | 40

## Slide 33: Applying DLP to Matrix Multiply
__m128 v3 = _mm128_set1_ps(0); int i; for(i = 0; i < arrlen/4*4;i+=4) { __m128 v1 = _mm128_load_ps(arr+i); __m128 v2 = _mm128_load_ps(arrtwo+i); v3 = _mm256_fmadd_ps(v1, v2, v3); } float mem[4] __attribute__ ((aligned (32))); _mm128_store(mem, v3); for(;i<arrlen;i++) { mem[0]+=arr[i]*arrtwo[i]; } return mem[0]+mem[1]+mem[2]+mem[3];

## Slide 34: Applying DLP to Matrix Multiply
One final optimization here: right now, we load two rows to yield one value. Each row gets loaded n times.
With enough vector registers, we can do this simultaneously to several cells at once
This uses 8 vector registers, but computes 4 cells with 4 loads: 2x fewer loads!
Does require an tail case for odd n
 |  |  |  |  | 17 | 21 | 25 | 29
 |  |  |  |  | 18 | 22 | 26 | 30
 |  |  |  |  | 19 | 23 | 27 | 31
 |  |  |  |  | 20 | 24 | 28 | 32
1 | 2 | 3 | 4 |  |  |  |  | 
5 | 6 | 7 | 8 |  |  |  |  | 
9 | 10 | 11 | 12 |  |  |  |  | 
13 | 14 | 15 | 16 |  |  |  |  | 

## Slide 35: Conclusion
Unfortunately, I couldn't get the code demo to work properly
  SIMD version kept being slower. Either I'm bad, I don't have SIMD vectors on this computer, or gcc is already SIMDing it for me. Probably the first one.
SIMD instructions are very useful when doing the same operation on a large array
Keep in mind that loads and stores to SIMD registers take a long time, so the goal is to keep the data in registers for as long as possible; otherwise you spend most of your time in loads/stores